AP Calc	WS#38 Volume of a Solid of Revolution -Cylindrical Shells Method	Name: ____

Suppose we want to rotate the region bounded by the curve y = 2x2 – x3	and y = 0 around the y-axis.

        →

Using disc method, we can see that having to find the radius R(y) by solving y = 2x2 – x3 for x, then use the Disc method is difficult. (It is doable for your extra credit). There is an easier method called Cylindrical Shells method and detail as below

Recall the formula of the cylinder of the cylinder shell below

If we let Δr = r2 – r1 and r = ½ (r2 + r1) (Average radius), then volume V = 2πrh Δr
End lecture.	Volume = (circumference)(height)(thickness)
Now, think of rotating y = f(x) (for a <x < b) about the y-axis to get the solid on the right.
When we divide the interval [a, b] into n subinterval rectangle of equal width Δx and f(xi) is the height, where xi is the midpoint. When rotating, each rectangle strip will create a cylinder shell, whose average radius r = xi; height h = f(xi) and thickness Δr = Δx. The volume of each shell by formula above is Vi = 2πrh Δr = 2π (xi) f(xi) Δx. The total volume obtain by taking limit of the sum as n → infinitive is	V = int from a to b 2%pi x f(x) dx	End lecture.

1. Find the volume of the region bounded by the curve y = 2x2 – x3 and y = 0 rotate around the y-axis
Picture on front page.	We found x-intercept at (0,0) and (2,0)
V = int from 0 to 1 2%pi x (2x^2 - x^3)dx = 2%pi int from 0 to 2 (2x^3 - x^4) dx =

2. Let S be the solid obtained by rotating the region shown in the figure about the y-axis. Show the x-intercept, find the volume and sketch the solid.

3. Find the volume of the solid obtained by rotating the region bounded by y = x – x2 and y = 0 about the line x = 2. Sketch the solid.

4. Find the volume of the solid obtained by rotating the region bounded by y = 7; y = x ½ ; x = 0 ; x = 4 bout the line x = 0. Sketch the solid.

5. Find the volume of the solid obtained by rotating the region bounded by y = – x2 + 7; y = x2 + 5 and about the line x = 3. Sketch the solid.